Fresh Concrete

and Mortar Application

Best Management Practices for the Construction Industry

Storm Drain Pollution

from Masonry and Paving

Fresh concrete and cement-related mortars that wash into lakes, streams, or estuaries are toxic to fish and the aquatic environment.  Disposing of these materials to the storm drains or creeks causes serious problems -- and is prohibited by law.

Storm Drain Pollution Prevention.

It’s Up to Us.

In San Mateo County, storm drains flow directly to local creeks, San Francisco Bay, and the Pacific Ocean with no treatment. Stormwater pollution is a serious problem for wildlife dependent on our waterways and for the people who live near polluted streams or wetlands. Some common sources of this pollution include spilled oil, fuel, and fluids from vehicles and heavy equipment; landscaping runoff containing pesticides or weed killers; and materials such as used motor oil, antifreeze, and paint products that people pour or spill into a street or storm drain.

All of the cities in San Mateo County have joined together with San Mateo County and the City/County Association of Governments (C/CAG) to educate local residents and businesses and fight storm drain pollution. We hope you will join us, by using the practices described in this pamphlet.

Who should use this brochure?

- Masons and bricklayers

- Sidewalk construction crews

- Patio construction workers

- Construction inspectors

- General contractors

- Home builders

- Developers

What Can You Do?

General Business Practices

- Both at your yard and the construction site, always store both dry and wet materials under cover, protected from rainfall and runoff. Protect dry materials from wind.

- Secure bags of cement after they are open. Be sure to keep wind-blown cement powder away from gutters, storm drains, rainfall, and runoff.

1

- Wash out concrete mixers only in designated wash-out areas in your yard, where the water will flow into containment ponds or onto dirt. Let concrete harden and dispose of as garbage. Whenever possible, recycle washout by pumping back into mixers for reuse. Never dispose of washout into the street, storm drains, drainage ditches, or streams.

During Construction

- Don’t mix up more fresh concrete or cement than you will use in a day.

- Set up and operate small mixers on tarps or heavy plastic drop cloths.

- When cleaning up after driveway or sidewalk construction, wash fines onto dirt areas, not down the driveway or into the street or storm drain.

- Prevent aggregate wash from driveway/patio construction from entering storm drains. Hose aggregate wash onto dirt areas and spade into dirt.

- Place hay bales or other erosion controls downslope to capture runoff carrying mortar or cement before it reaches the storm drain.

- When breaking up paving, be sure to pick up all the pieces and dispose properly.

- Recycle large chunks of broken concrete at a landfill.

- Dispose of small amounts of excess dry concrete, grout, and mortar in the trash.

- Never bury solid or hazardous waste material.

San Mateo Countywide Stormwater Pollution Prevention Program (STOPPP)

555 County Center

Redwood City, CA 94063

STOPPP gratefully acknowledges the Santa Clara Valley  Nonpoint Source Pollution Program for the original concept and text of this brochure.